## Slide 1: Proactive Network Maintenance and Signal Leakage

## Slide 2: Agenda
Proactive Network Maintenance (PNM)
  Impedance Mismatch
  Micro-Reflections
  US Frequency Response & Pre-EQ Tap Display
The Marriage
  Pressure Testing
  Shielding Integrity
  Successes

## Slide 3: A PNM Goal Frequency Response ≤ 0.5 dB Each Bonded Channel
All PNM Traces Courtesy Nimble This (Brady Volpe)
Notes: Two channels capable of bonding
Frequencies close enough so that path disturbances should look similar in both channels
Minimize impedance discontinuities
Not practical to eliminate all the wrinkles

## Slide 4: Nominal Impedance Measles Chart
Notes: Every device and every connection presents a mismatch opportunity
All devices and the interconnecting cable specified to have a NOMINAL impedance of 75 ohms.
Explain Return Loss specification

## Slide 5: Creating Micro-Reflections
Fiber Node
Notes: Discuss distances without mentioning echo tunnels

## Slide 6: The CMTS Challenge Modem to CMTS US Frequency Response
All PNM Traces Courtesy Nimble This (Brady Volpe)
Notes: During registration, the modem sees this frequency response
Sends correcting coefficients to the modem’s pre-equalizer

## Slide 7: CMTS Solution CMTS to MODEM Pre-Equalizer Correction
All PNM Traces Courtesy Nimble This (Brady Volpe)
Notes: Describe the chart
Taps
Coefficients
Math Lesson next

## Slide 8
😱
JUST KIDDING 🤡

## Slide 9: Transmission Speed
64-QAM US Symbol Rate = 5.12 mega-symbols/second (ms/s)
1 symbol transmitted every 1 / 5.12E6 = 195.3E-9 or 195.3 nanoseconds (nsec)
One-way trip @ VOP = 87 %, (195.3 x 0.87) = 169.9 / 2 = 84.995 nsec
Notes: OFDMA will be quite different.

## Slide 10: Speed of Light
186,282.4 Miles per second (in a vacuum)
  < 5th century assumed infinite
  5th century Empedocles questioned the assumption
  6th century Aristotle disagreed – back to infinite
  1629 Isaac Beeckman used mirrors and exploding gunpowder
  1638 Galileo used lanterns spaced at known distances
  1676 Römer studied Jupiter’s moons & earth’s diameter (27%)
  1729 Bradley improved the accuracy but Römer wins the honor
  And then, along came lasers - filled in the 27%
Notes: 5th century Empedocles questioned SOL was infinite
6th century Aristotle disagreed
1629 Isaac Beeckman experimented with mirrors and exploding gunpowder
1638 Galileo proposed using lanterns at some known distance
1676 Römer studied Jupiter’s moons and used the diameter of Earth got within about 27%
1729 Bradley improved on the accuracy, but Römer wins the honor of proof.
Information necessary to understand the Echo Tunnel Concept

## Slide 11: Speed of Light
186,282.4 Miles per second (in a vacuum)
186,282.4 x 5,280 = 983,571,056 feet per second
1 / 983,571,056 = 1.0167 nanoseconds per foot
Conclusion
  Since 1 symbol is transmitted every 84.995 nsec, and
  there is 1 Pre-Equalizer Tap per symbol, and
  traveling speed is 1 nsec/foot,
  the distance between Pre-EQ bars is about 85 feet.
Notes: 5th century Empedocles questioned SOL was infinite
6th century Aristotle disagreed
1629 Isaac Beeckman experimented with mirrors and exploding gunpowder
1638 Galileo proposed using lanterns at some known distance
1676 Römer studied Jupiter’s moons and used the diameter of Earth got within about 27%
1729 Bradley improved on the accuracy, but Römer wins the honor of proof.
Information necessary to understand the Echo Tunnel Concept

## Slide 12: Echo Tunnel Concept
All PNM Traces Courtesy Nimble This (Brady Volpe)
Notes: Each bar represents the proportion of input signal routed through fixed-delay Equalizer Taps (not to be confused with House Taps)
Spacing between bars is about…85 feet.

## Slide 13: Clustering or Not
Independent
Clustered

## Slide 14: Pressure Testing Tools
M3 Signal Source
Compass
Leakage Detector

## Slide 15: Pressure Testing
Triple Frequency Scan
M3 Generates a unique marker at +40 or +60 dBmV
Detects sources of drop system flaws with shielding integrity > 120 dB
Allows detecting integrity flaws without entering customer premise
TV
TV
TV
M3 Marker signal
VHF and UHF

## Slide 16: Shielding Integrity About 40 reasons to Maintain
Power lines & their hardware (hum, arc, spark, corona buzz, • AC light dimmers • Electric fences • Computers + all microprocessors with digital clocks (oscillator) • Brush-type motors (vacuum, sewing machine, power tools) • Thermostats, power controllers, motor controllers (washer, dryer, fridge, etc.) • Fluorescent lights, touch lights, neon lights • Bug zappers, electric fences, ignition pulses • Cordless phones, baby monitor • Weird stuff: doorbell transformer, electric blanket, fish tank thermostat DVD + Blu-Ray players • In-line or “wall-wart”-type laptop power supplies (especially switcher-type) • Newer front-loading washing machines • Computers, tablets, smart phones (some good, some BAD!) • Plasma flat-screen TVs (most BAD) • Automotive engine computers (some) • ADSL box/desktop computer combination • ”Touch” –controlled lights, faucets, etc. • “Coil”-type fluorescent bulbs –some quiet, some bad • Wireless modem jacks, digital cable converters • LED light assemblies for house lighting (120 VAC)

## Slide 17: PNM: Elevated Taps 9 & 10 Can Indicate an In-Home Issue
Single Home with No Network Leakage Points to an In-Home Problem
Problem: Damaged cable inside wall plate
Chart: Bad Modem EQ Taps
 | -46.19 | -43.08 | -39.03 | -35.52 | -31.27 | -27.42 | -22.12 | -0.38 | -11.99 | -20.69 | -26.75 | -31.37 | -34.36 | -37.42 | -41.33 | -45.26 | -46.34 | -47.6 | -51.45 | -56.25 | -54.63 | -48.75 | -47.41 | -52.42
Chart: Good Modem EQ Taps
 | -60 | -53.22 | -54.28 | -47.67 | -48.68 | -40.41 | -29.81 | -0.01 | -28.87 | -40.28 | -43.58 | -46.52 | -56.01 | -52.32 | -55.8 | -52.6 | -57.8 | -52.96 | -54.43 | -60 | -60 | -56.62 | -59.92 | -60

## Slide 18
A cluster of homes with elevated taps indicates a possible network shielding flaw Issue.
Chart: House 1
 | -60 | -53.22 | -54.28 | -47.67 | -48.68 | -40.41 | -29.81 | -0.01 | -28.87 | -40.28 | -43.58 | -46.52 | -56.01 | -52.32 | -55.8 | -52.6 | -57.8 | -52.96 | -54.43 | -60 | -60 | -56.62 | -59.92 | -60
Chart: House 2
 | -60 | -53.22 | -54.28 | -47.67 | -48.68 | -40.41 | -29.81 | -0.01 | -28.87 | -40.28 | -43.58 | -46.52 | -56.01 | -52.32 | -55.8 | -52.6 | -57.8 | -52.96 | -54.43 | -60 | -60 | -56.62 | -59.92 | -60
Chart: House 3
 | -60 | -53.22 | -54.28 | -47.67 | -48.68 | -40.41 | -29.81 | -0.01 | -28.87 | -40.28 | -43.58 | -46.52 | -56.01 | -52.32 | -55.8 | -52.6 | -57.8 | -52.96 | -54.43 | -60 | -60 | -56.62 | -59.92 | -60
These homes exhibit elevated taps 11 through 15
Problem found: Crack in the hardline
PNM Data Provides Clues to the Location of the Problem
PNM: Higher Numbered Taps Can Indicate A Network Issue

## Slide 19
Home 1
Problem Found: In-Line Drop Splice with Corroded Crimp Connector
Before
After

## Slide 20
Home 2
Problems Found: Flawed connector makeup in buried splice enclosure resulting in corroded connectors and bad drop filter in pedestal
Before
After

## Slide 21
Home 3
Problems Found: Bad splitter with twist-on connectors
Elevated taps to the left of the main tap indicates group delay and is likely a network problem.
Before
After

## Slide 22
Chart: Bad Primary EQ Taps
 | -46.19 | -43.08 | -39.03 | -35.52 | -31.27 | -27.42 | -22.12 | -0.38 | -11.99 | -20.69 | -26.75 | -31.37 | -34.36 | -37.42 | -41.33 | -45.26 | -46.34 | -47.6 | -51.45 | -56.25 | -54.63 | -48.75 | -47.41 | -52.42
PNM and M3/Compass Field Test Results
➕
15 homes in this study; 100% had cable defects that were identified by the M3/Compass
Cable defects detected with the M3/Compass resolved micro-reflection issues in 13/15 (87%).
  Two homes had issues with in-line filters that were unidentifiable until leakage was resolved.
PNM and M3/Compass can dramatically improve technician troubleshooting effectiveness

## Slide 23: Conclusion
The marriage between Proactive Network Maintenance techniques and Pressure Testing drop system wiring proves an all-out winner by providing the means to identify, locate and fix issues well before the customer becomes aware of an issue.